## Slide 1: Goals for today’s lecture
By the end of today’s lecture, you should be able to:
write C code to control pixels on an LCD matrix display
describe the concept of structured design
describe Unified Markup Language tools developed for system design
produce a UML state diagram to describe your project design concept
produce a specifications requirements document
begin work on your embedded system design document

## Slide 2: Verification vs Validation
Validation: DONE FIRST!
  Does your specification meet customer intent
  Each requirement from the customer (your professor) should be reviewed
  Some requirments may bedome multiple requirements
Verification
  Does your product meet the requirement as you defined it?

## Slide 3: The SYstem Requirements Specification
What you need to do:
You will work in groups of 2 on the final project
Get with your partner and decide what your design must accomplish
  The core requirements use the key word “must”*
  the extra features use the key word “may”
  Number the requirements
Write the System Requirements Specification document with the following parts:
  Introduction with purpose and goals of your embedded system
  A block diagram showing the major components
  A “walk through” of the user interface
  A list of requirements written as described in the previous slide
  A verification method for each requirement
  A timeline for the project with weekly milestones

## Slide 4: Defining your requirements
REMEMBER- these are what YOU are signing up for- not the customer requirements.
WHY are requirements important?
Building something before you design it results in wasted material and time.
Disagreements among team members
Chart: Requirement Issues
| Incorrect Facts | Missing | Inconsistant | Ambiguous | Misplaced
 | 49 | 31 | 13 | 5 | 2

## Slide 5: Defining your requirements
Chart: Relative Cost of Changing Requirements
| Requirements | Design | Coding | Development | integration of SW and HW | Field Test
 | 1 | 3 | 10 | 15 | 30 | 40
Why is it so hard?
Inconstant needs
Impossible wants
Obsession with bigger and better
Time crunch
Mistakes don’t seem like a big deal now
Just wing it
Obsessed with latest and greatest
Notes: Time crunch- we want everthing now

## Slide 6: Capturing requirements
First, workout scenarios on how your product might work
Identify interfaces to rest of the world (Web, Sensors, Buttons..
Write down rationale for each requirement!
Develop hierarchy- so subsystems can be described as part of a bigger system- helping traceability.
Can each requirement be verified on its own?
(Quicker way to finish)
BASELINE!

## Slide 7: Writing GOOD requirements
What do you want to eat?
  Something good
  Something cheap
  Anything without tomatoes.
Each answer is a requirement that is up to interpretation.
Requirements define something that is NEEDED

## Slide 8: Writing GOOD requirements
VERIFIABLE
  Test
  Inspection
  Analysis
ATTAINABLE
  Electrical/computer/mechanical/production
CLEAR
  Simple
  Short (no long explanations)
  Positive (limit negative requirements)
    Hard to verify that something does not happen
    Easier to verify that something does happen

## Slide 9: Common Requirement Mistakes
Making Assumptions (especially the bad kind)
  Assuming the customer agrees or knows risks
Don’t design! Limit writing how to do something- just what is needed.
  Limits how implementation may be accomplished
Define what an operator must do.
  Define product requirements- not people requirements
Use ambiguous terms
  “et cetera”, “etc”, “as needed”, “and/or”…
Bad Grammar
Unverifiable
  Wastes time at the end!
  “sufficient”, “adequate”,”easily”, “often”, “user-friendly”

## Slide 10: Verification
Each Requirement should have a verification method (use a matrix!)
MOST methods should be “TEST”
  If the requirement defines an action and a result
  = TEST!
Define all Verification methods when requirements are complete- but BEFORE implementation!!!
Analysis requirements are usually used for “testable” items that aren’t easily tested
(cost, time)
Notes: Will operate in normal environment
Must use I2C to communicate between processors
Life vest shall be warn by individuals

## Slide 11: Developing a System Architecture
Describing an embedded system’s behavior
  Unified Modeling Language (UML) was developed as a computer science standard to develop object-oriented system design (and is used in other areas)
  One tool, a state machine diagram (statechart), is used for modeling system behavior through finite state transitions.
  This will be a useful tool in developing your embedded system design

## Slide 12: System Architecture – UML Statechart Diagram
state nodes connected with transitions triggered by events
models dynamic aspects of a system
models how the system reacts to inputs
describes different states of the system
defines a state machine to model the system

## Slide 13: UML Behavioral State Machine
In extending the finite state machine structure
  A state models a situation during which some condition holds.
    a static situation such as an object waiting for some external event to occur.
      the event is said to “trigger” an action
    a dynamic conditions such as the process of performing some behavior.
    enters the state when the behavior commences and leaves it as soon as the behavior is completed
  The UML defines the following kinds of states:
    simple state,
    composite state.

## Slide 14: UML Behavioral State Machine
A simple state is a state that does not have sub states.
Drawn as a rectangle with rounded corners and the state name inside the rectangle.
  Simple state may have compartments:
    name compartment
    internal activities compartment
      holds a list of internal actions or state activities that are performed while in the state
      activity label identifies the circumstances under which the behavior will be invoked.

## Slide 15
A composite state is defined as state that has sub states
Composite state will have the following:
  name compartment
  internal activities compartment
  “decomposition compartment” (sub state sequence)
The first two compartments are the same as for simple state.
Decomposition refers to the nested structure of the state, diagrammed with internal states and transitions.
UML Behavioral State Machine

## Slide 16
If a large number of states are inside a composite state, they may not fit in the graphical space available for the diagram.
In that case, use a simple state graphic with a special "composite" icon.
This icon is a visual cue that the state has a decomposition that is not shown.
The contents of the composite state are shown in a separate diagram (could be on a different page)
UML Behavioral State Machine

## Slide 17
An initial pseudostate represents the symbol for a transition to the initial or default state.
An initial pseudostate is shown as a small solid filled circle.
Final state is a special kind of state signifying that the enclosing region (e.g., composite state) is completed.
E.g.,
UML Behavioral State Machine

## Slide 18
A transition is a directed relationship between a source state and a target state.
Transitions between states
  Reflect change in system from one state to another
  Expressed as an arrow directed from source to destination
Transition occurs when
  Event of interest to system occurs (triggered transition)
  System has completed some action and is ready to move to next state (triggerless transition)
An action may be associated with the the transition, or it may be a transition to self
UML Behavioral State Machine

## Slide 19: UML Behavioral State Machine
from http://www.uml-diagrams.org
If the test fails, ATM goes into Out of Service state, otherwise there is triggerless transition to the Idle state.
In this state ATM waits for customer interaction.
The ATM state changes from Idle to Serving Customer when the customer inserts banking or credit card in the ATM's card reader.
On entering the Serving Customer state, the entry action readCard is performed.
The transition from Serving Customer state back to the Idle state could be triggered by cancel event or final state
Top level state machine Bank ATM is initially turned off. After the power is turned on, ATM performs startup action and enters Self Test state.

## Slide 20: UML Behavioral State Machine
from http://www.uml-diagrams.org
Customer Authentication and Transaction are composite states by themselves which is shown with hidden decomposition indicator icon.
Serving Customer state has triggerless transition back to the Idle state after transaction is finished.
The state also has exit action ejectCard which releases customer's card on leaving the state, no matter what caused the transition out of the state.
Serving Customer state is a composite state with sequential sub states Customer Authentication, Selecting Transaction and Transaction.

## Slide 21: Describing a system as a state machine
  List all possible states
  Declare all variables
  For each state, list possible transitions, with conditions, to other states
  For each state and/or transition, list associated actions
  For each state, ensure exclusive and complete exiting transition conditions
    No two exiting conditions can be true at same time
      Otherwise, nondeterministic state machine
    One condition must be true at any given time
Here’s a couple of examples of a free drawing tools to support making UML behavioral state diagrams
https://wiki.gnome.org/action/show/Apps/Dia?action=show&redirect=Dia
http://argouml.tigris.org/

## Slide 22: Software Implementation of State Machine
#define S0 0
#define S1 1
...
#define SN N
void StateMachine() {
int state = S0; // or whatever is the initial state.
while (1) {
switch (state) {
case S0:
// Insert S0’s actions here & Insert transitions Ti leaving S0:
if( T0’s condition is true ) {state = T0’s next state; /*actions*/ }
if( T1’s condition is true ) {state = T1’s next state; /*actions*/ }
...
if( Tm’s condition is true ) {state = Tm’s next state; /*actions*/ }
break;
case S1:
// Insert S1’s actions here
// Insert transitions Ti leaving S1
break;
...
case SN:
// Insert SN’s actions here
// Insert transitions Ti leaving SN
break;
}
}
}