## Slide 1: Topics for today’s lecture
Analyze three analog circuit models for a digital logic output stage
Establish a digital output stage’s ability to source and sink current
  What is meant by “output contention”
Open collector/drain outputs
Output enabled gates

## Slide 2: Digital Logic Output Models
An ideal logic gate has only two output voltage levels
and can be represented by an ideal circuit voltage supply model
What happens when vin is between 0 and 5 V, say 2.5V?
Can the output act like an ideal voltage source with unlimited current?

## Slide 3: Digital Logic Output Models
Output stage for a standard TTL logic gate
- State: driven high (lower transistor is off)

## Slide 4: Digital Logic Output Models
vout = +5V − 100 · iout − Vce − Vd
iout : current flowing out of the output pin
Vce : collector-to-emitter voltage drop across the transistor, which depends on iout
Vd : voltage drop across the diode, which also depends on iout
Some important observations are:
The output high voltage ≠ +5V
The output voltage will depend upon the output current.
The output pin will be a source of current.
Equivalent circuit model for a standard TTL device while driving high, i.e., sourcing current

## Slide 5: Digital Logic Output Models
Output stage for a standard TTL bi-polar and a model of the output when driven low (upper transistor is off)

## Slide 6: Digital Logic Output Models
The output voltage vout will be Vce, the voltage drop across the bottom transistor
The output low ≠ 0V
The output voltage will depend upon the output current iout
The output pin must be able to sink current to ground.
Equivalent circuit model for a standard TTL device while driving low, i.e., sinking current

## Slide 7: Digital Logic Output Models
iout refers to the current flowing :
into the gate (when driving low) or
out of the gate (when driving high)
Positive (+) iout flows into the gate.
Negative (-) iout flows out of the gate.
If iout = 2.5mA, then the device is driving low and sinking 2.5mA to ground.
if iout = −1mA, then the device is driving high and sourcing 1mA from +5V.

## Slide 8: Digital Logic Output Models
This output stage is called a push-pull stage, since it is capable of both sourcing (“pushing”) and sinking (“pulling”) current.
Another name for this output stage is a totem-pole driver, since the two transistors and diode stacked on top of one another resemble a totem pole.
Another form of output stage can only sink current, an open-collector or open-drain output stage.

## Slide 9: Digital Logic Output Models
The relationship between output voltage and current is very non-linear
These plots are from the IBIS (I/O Buffer Information Spec) models for a SN74ALS04 inverter published by the device manufacturer
Typical output voltages plotted against input current for a 74ALS04 inverter.

## Slide 10: Digital Logic Output Models
Ex. calculate a value for R1 to provide 20mA to light the LED that has a forward voltage Vf of 1.5 V.
From the IBIS chart, the output voltage of the inverter is approximately Vout = 3.1V when sourcing 20mA
Power Dissipated in chip = (5 − 3.1) · 0.02 = 38mW
  could overheat if all 6 inverters are driving LEDs

## Slide 11: Digital Logic Output Models
Many modern microcontrollers specifically boast that their digital I/O pins can directly drive LED’s.
For example, for the MSP432, 4 of the I/O pins can source or sink up to 20 mA (the rest only 6 mA)
Other devices may drive up to 40 mA (e.g., ATmega 328P)
You must still consider the total power dissipation of the device
The microcontroller datasheet will typically contain limits on how much total current can flow into and out of the VCC pins.
E.g., total max current for the ATmega 328P between VCC and ground is 200 mA according to the data sheet.

## Slide 12: Digital Logic Output Models
A CMOS logic gate output circuit
When output is driven high, vout = +5V − iout · RDS(on)
Since RDS(on) (the drain-source resistance when MOSFET is on) is small, the output voltage as a function of current will look different than for a BJT

## Slide 13: Digital Logic Output Models
Output voltage vs. current for CMOS logic gate

## Slide 14: Digital Logic Output Models
While clearly non-linear, voltage-current characteristic of digital output stages is nearly linear over a limited range of current values
At relatively low currents (below 20mA), a digital output stage can be reasonably well approximated as shown above

## Slide 15: Digital Logic Output Models
Output resistances tend to be lower for sinking current and higher for sourcing current.
What does this say about “driving” an output (sink or source)?

## Slide 16
Digital Logic Output Models
ex., turn on a panel light when logic signal X goes to logic 1
design for current of 20 mA
panel light on resistance modeled as 150 W and 3V drop
use linear model for 74AHC04 output stage sinking current with logic signal X at logic 1,
to get current of 20 mA,
power dissipated in gate is

## Slide 17
Digital Logic Output Models
Connecting two outputs together like this should not be done!
Output Contention
to see why this can create problems, substitute the output models

## Slide 18
Digital Logic Output Models
Problem with tying two CMOS gate outputs together when one is driving high and the other driving low
Same problem exists for BJT outputs on TTL gates

## Slide 19
Digital Logic Output Models
Versions of gates exist without the upper transistor on output
Open collector device (a) and open drain device (b)
Can drive low, to sink current, but when transistor is off the output is floating (said to be in high impedance state)
Therefore, it cannot drive current to a load!

## Slide 20
Digital Logic Output Models
Open collector inverter output “floats” for logic low input
Note the special symbol designating open collector (or drain)
The 74LS05 is an open collector version of the 74LS04 inverter

## Slide 21
Digital Logic Output Models
Add pull-up R to open drain output
When output goes low, 74LS05 will draw (5-vout)/R current
This results in wasted power as long as output is low
When output floats, next gate sees about 5V due to pull-up R
Why bother with open collector (drain) outputs?

## Slide 22
Digital Logic Output Models
You were told it was a bad thing to connect gate outputs, but,
these open drain inverter outputs can implement a NOR function without an additional gate
Note: neither gate can source current, so we don’t have a contention problem

## Slide 23
Digital Logic Output Models
Open drain inverting outputs on peripherals enable simple signaling (asserted low)
Note: could add several more peripheral open drain outputs with no hardware modification!
virtual NOR gate

## Slide 24
Digital Logic Output Models
Bi-directional communication
The I2C communications protocol implements an interface between a microcontroller and multiple peripheral devices using 2 wires (plus ground)

## Slide 25
Digital Logic Output Models
Output voltage level shifting
Driving devices that require
higher voltage

## Slide 26
Digital Logic Output Models
Drawback of open collector(drain) gates:
when driven low they have quick response
when pulled high, the output experiences an RC charge curve

## Slide 27
Digital Logic Output Models
Output enabled gates
Some gates have all three output states (tri-state outputs)
Several microcontrollers make good use of them

## Slide 28
Digital Logic Output Models
output enabled gates used for dual purposing a microcontroller bi-directional I/O pin controlled by the DIR register bit
DIR

## Slide 29
Digital Logic Output Models
Example of a 74AHC245 transceiver using output enabled gates
DIR controls direction of data flow from source A or source B

## Slide 30
In summary,
understand how the transistor output stage affects gate operation
output contention is bad
open collector (drain) outputs overcome contention and are useful for implementing practical interfaces
tri-state outputs commonly used in microcontrollers to repurpose limited number of I/O pins
Digital Outputs