## Slide 1: Basic Master Mode SPI C Code
From ST7735.c, Adafruit library modified by Daniel Valvano (in the archive you can download from
http://edx-org-utaustinx.s3.amazonaws.com/UT601x/ValvanoWare.zip )
// ST7735.c
// Runs on MSP432
// Low level drivers for the ST7735 160x128 LCD
// Backlight (pin 10) connected to +3.3 V  pin 8, has a small series resistor
// MISO (pin 9) unconnected
// SCK (pin 8) connected to P9.5 (UCA3CLK)  pin 7
// MOSI (pin 7) connected to P9.7 (UCA3SIMO)  pin 6 *** labeled SDA ***
// TFT_CS (pin 6) connected to P9.4 (UCA3STE) pin 3 labeled CS
// CARD_CS (pin 5) unconnected
// Data/Command (pin 4) connected to P9.2 (GPIO), high for data, low for command
 pin 5 *** labeled A0 ***
// RESET (pin 3) connected to P9.3 (GPIO)  pin 4
// VCC (pin 2) connected to +3.3 V  pin 1 *** be very careful not to switch VCC and GND !!!
// Gnd (pin 1) connected to ground  pin 2
The example code we’re suggesting you start with was written for a different implementation of a ST7735 module, therefore, there are some pin location and name differences.