## Slide 1
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Introduction to Digital Systems
EGR 226
Lecture_3

## Slide 2: Objectives for today’s lecture
After today’s lecture you should be able to:
Describe MSP432 port I/O configuration and usage
Compare HW and SW switchbounce methods
Review use of the ARM SysTick timer peripheral on the MSP432 to generate precise time intervals
Review implementation and execution of interrupt routines for Systick and GPIO
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 3: Embedded system architecture
micro
controller
power
supply
digital
actuators
digital
inputs
display
timers
inter-process
communication
analog
actuators
Inputs
Processing and Control
Outputs
memory
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
A/D
converter
D/A
converter
analog
sensors

## Slide 4
P1.0, P1.2, P1.3, P2.0, P2.1, P2.2,
P3.1, & P3.4 are available on jumpers,
P1.1, P1.4, P8.1 are not)
MSP432
Architecture
General-Purpose I/O (GPIO):
78 pins
10 ports
Pins are multiplexed between
std I/O and peripherals
Only 67 pins are available
G
P
I
O
P
o
r
t
3
e
U
S
C
I
P
1
.
7
/
U
C
B
0
S
C
L
P
1
.
6
/
U
C
B
0
S
D
A
P
1
.
5
/
U
C
B
0
C
L
K
P
1
.
4
/
U
C
B
0
S
T
E
P
1
.
3
/
U
C
A
0
T
X
D
P
1
.
2
/
U
C
A
0
R
X
D
P
1
.
1
/
U
C
A
0
C
L
K
P
1
.
0
/
U
C
A
0
S
T
E
P
2
.
7
/
T
A
0
.
4
P
2
.
6
/
T
A
0
.
3
P
2
.
5
/
T
A
0
.
2
P
2
.
4
/
T
A
0
.
1
P
2
.
3
/
U
C
A
1
T
X
D
P
2
.
2
/
U
C
A
1
R
X
D
P
2
.
1
/
U
C
A
1
C
L
K
P
2
.
0
/
U
C
A
1
S
T
E
P
3
.
7
/
U
C
B
2
S
C
L
P
3
.
6
/
U
C
B
2
S
D
A
P
3
.
5
/
U
C
B
2
C
L
K
P
3
.
4
/
U
C
B
2
S
T
E
P
3
.
3
/
U
C
A
2
T
X
D
P
3
.
2
/
U
C
A
2
R
X
D
P
3
.
1
/
U
C
A
2
C
L
K
P
3
.
0
/
U
C
A
2
S
T
E
P
4
.
7
/
A
6
P
4
.
6
/
A
7
P
4
.
5
/
A
8
P
4
.
4
/
A
9
P
4
.
3
/
R
T
C
C
L
K
/
A
1
0
P
4
.
2
/
T
A
2
C
L
K
/
A
1
1
P
4
.
1
/
A
1
2
P
4
.
0
/
A
1
3
P
5
.
7
/
T
A
2
.
2
P
5
.
6
/
T
A
2
.
1
P
5
.
5
/
A
0
P
5
.
4
/
A
1
P
5
.
3
/
A
2
P
5
.
2
/
A
3
P
5
.
1
/
A
4
P
5
.
0
/
A
5
e
U
S
C
I
P
6
.
7
/
T
A
2
.
4
/
/
U
C
B
3
S
C
L
P
6
.
6
/
T
A
2
.
3
/
U
C
B
3
S
D
A
P
6
.
5
/
U
C
B
1
S
C
L
P
6
.
4
/
U
C
B
1
S
D
A
P
6
.
3
/
U
C
B
1
C
L
K
P
6
.
2
/
U
C
B
1
S
T
E
P
6
.
1
/
A
1
4
P
6
.
0
/
A
1
5
P
7
.
7
/
T
A
1
.
1
/
C
0
.
2
P
7
.
6
/
T
A
1
.
2
/
C
0
.
3
P
7
.
5
/
T
A
1
.
3
/
C
0
.
4
P
7
.
4
/
T
A
1
.
4
/
C
0
.
5
P
7
.
3
/
T
A
0
.
0
P
7
.
2
/
C
1
O
U
T
/
T
A
1
C
L
K
P
7
.
1
/
C
0
O
U
T
/
T
A
0
C
L
K
P
7
.
0
/
S
M
C
L
K
/
D
M
A
E
0
P
8
.
7
/
A
1
8
P
8
.
6
/
A
1
9
P
8
.
5
/
A
2
0
P
8
.
4
/
A
2
1
P
8
.
3
/
T
A
3
C
L
K
/
A
2
2
P
8
.
2
/
T
A
3
.
2
/
A
2
3
P
8
.
1
/
U
C
B
3
C
L
K
/
T
A
2
.
0
P
8
.
0
/
U
C
B
3
S
T
E
/
T
A
1
.
0
P
9
.
7
/
U
C
A
3
T
X
D
P
9
.
6
/
U
C
A
3
R
X
D
P
9
.
5
/
U
C
A
3
C
L
K
P
9
.
4
/
U
C
A
3
S
T
E
P
9
.
3
/
T
A
3
.
4
P
9
.
2
/
T
A
3
.
3
P
9
.
1
/
A
1
6
P
9
.
0
/
A
1
7
P
1
0
.
5
/
T
A
3
.
1
/
C
0
.
6
P
1
0
.
4
/
T
A
3
.
0
/
C
0
.
7
P
1
0
.
3
/
U
C
B
3
S
C
L
P
1
0
.
2
/
U
C
B
3
S
D
A
P
1
0
.
1
/
U
C
B
3
C
L
K
P
1
0
.
0
/
U
C
B
3
S
T
E
C
o
r
t
e
x
M
4
S
y
s
t
i
c
k
N
V
I
C
P
e
r
i
p
h
e
r
a
l
B
u
s
T
i
m
e
r
A
S
y
s
t
e
m
B
u
s
I
n
t
e
r
f
a
c
e
G
P
I
O
P
o
r
t
1
e
U
S
C
I
G
P
I
O
P
o
r
t
5
A
D
C
1
4
G
P
I
O
P
o
r
t
2
G
P
I
O
P
o
r
t
4
A
D
C
1
4
T
i
m
e
r
A
G
P
I
O
P
o
r
t
6
A
D
C
1
4
T
i
m
e
r
A
e
U
S
C
I
G
P
I
O
P
o
r
t
7
T
i
m
e
r
A
G
P
I
O
P
o
r
t
8
A
D
C
1
4
e
U
S
C
I
G
P
I
O
P
o
r
t
9
A
D
C
1
4
e
U
S
C
I
G
P
I
O
P
o
r
t
1
0
T
i
m
e
r
A
e
U
S
C
I
T
i
m
e
r
A
T
i
m
e
r
A
T
i
m
e
r32
R
T
C
Almost 32
ADC Channels

## Slide 5: Partial Table of Alternate Pin Functions
Pin | PxSEL1=0, PxSEL0=0 | PxSEL1=0, PxSEL0=1 | PxSEL1=1, PxSEL0=0 | PxSEL1=1, PxSEL0=1
P1.0 | Port | UCA0STE |  | 
P1.1 | Port | UCA0CLK |  | 
P1.2 | Port | UCA0RXD/UCA0SOMI |  | 
P1.3 | Port | UCA0TXD/UCA0SIMO |  | 
P1.4 | Port | UCB0STE |  | 
P1.5 | Port | UCB0CLK |  | 
P1.6 | Port | UCB0SIMO/UCB0SDA |  | 
P1.7 | Port | UCB0SOMI/UCB0SCL |  | 
P2.0 | Port | UCA1STE |  | 
P2.1 | Port | UCA1CLK |  | 
P2.2 | Port | UCA1RXD/UCA1SOMI |  | 
P2.3 | Port | UCA1TXD/UCA1SIMO |  | 
P2.4 | Port | TA0.CCI1Aa / TA0.1b |  | 
P2.5 | Port | TA0.CCI2Aa / TA0.2b |  | 
P2.6 | Port | TA0.CCI3Aa / TA0.3b |  | 
P2.7 | Port | TA0.CCI4Aa / TA0.4b |  | 
P3.0 | Port | UCA2STE |  | 
P3.1 | Port | UCA2CLK |  | 
P3.2 | Port | UCA2RXD/UCA2SOMI |  | 
P3.3 | Port | UCA2TXD/UCA2SIMO |  | 
P3.4 | Port | UCB2STE |  | 
P3.5 | Port | UCB2CLK |  | 
P3.6 | Port | UCB2SIMO/UCB2SDA |  | 
P3.7 | Port | UCB2SOMI/UCB2SCL |  | 
P4.0 | Port |  |  | A13
P4.1 | Port |  |  | A12
P4.2 | Port | ACLKb | TA2CLKa | A11
P4.3 | Port | MCLKb | RTCCLKb | A10
P4.4 | Port | HSMCLKb | SVMHOUTb | A9
P4.5 | Port |  |  | A8
P4.6 | Port |  |  | A7
P4.7 | Port |  |  | A6
SEL1 and SEL0 bits on the MSP432 specify alternate functions.
P1.2 and P1.3 are hardwired to the serial port to USB interface.
Table 4.1 in Valvano’s textbook
Default Primary Secondary Tertiary
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
General Purpose I/O
Primary Module Function
Secondary Module Function
Tertiary Module Function
0
1
2
3
MUX bits of
PxSEL0 & PxSEL1
Pin of Chip

## Slide 6: Switch Bounce
A hardware approach to controlling switch bounce
http://web.engr.oregonstate.edu/~traylor/ece473/lectures/debounce.pdf

## Slide 7: Switch bounce delays

## Slide 8: Switch Bounce
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
+
3
.
3
V
1
0
k
W
Switch
Decision making at the
right time ~>50ms
Switch is open
the analog voltage measured on a momentary switch
Switch is
closed
Switch
is open
Ideal case
Open / +5V
Close / 0V
Open / +5V
Causes LED output to toggle if making decision at the wrong instant

## Slide 9: Code
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
while(1)
{
if(DebounceSwitch1())
P1OUT ^= BIT0; //Toggle P1 LED
}
#include "msp.h"
void main(void)
{
WDT_A->CTL = WDT_A_CTL_PW | WDT_A_CTL_HOLD; // stop watchdog timer
while ( 1 )
{
……………………………………… ;
}
}
uint8_t DebounceSwitch1(void) // Switch on Port P1.1
{
static uint16_t State = 0;
State = (State<<1) | ((P1IN & BIT1)>>1) | 0xfc00;
__delay_cycles(5);
if(State == 0xfc00)
return 1;
return 0;
}

## Slide 10: Switch Bounce
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
// Service routine called at regular timer intervals
uint8_t DebounceSwitch1()
{
static uint16_t State = 0; // Current debounce status
// read switch, upper 5 bits of State are don't cares
State=(State<<1) | (P1IN & 0x2)>>1 | 0xf800;
__delay_cycles(5);
if(State==0xfc00)return 1; // indicates 0 level is stable for 10 consecutive calls
return 0;
}
pass switch line value of State return
1 pulled up 1111 1000 0000 0001 0
10 pulled up 1111 1011 1111 1111 0
n switch pressed 1111 1111 1111 1110 0
n+1 switch bounce 1111 1111 1111 1101 0
n+2 switch bounce 1111 1111 1111 1010 0
n+3 switch bounce 1111 1111 1111 0101 0
n+4 switch press stable 1111 1111 1110 1010 0
n+5 switch press stable 1111 1111 1101 0100 0
n+10 switch press stable 1111 1100 0000 0000 1
n+11 switch press stable 1111 1000 0000 0000 0

## Slide 11: Code
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
while(1)
{
if( DebounceSwitch1())
P1OUT ^= BIT0; //Toggle P1 LED
}
#include "msp.h"
void main(void)
{
WDT_A->CTL = WDT_A_CTL_PW | WDT_A_CTL_HOLD; // stop watchdog timer
while ( 1 )
{
……………………………………… ;
}
}
int DebounceSwitch1(void)
{
int pin_Value = 0; //initialize variable as low
if ((P1IN & 0x02) == 0x00) //check of button pushed
{ __delay_cycles(30000); //pause for 10 m-sec for switch bounce
if ((P1IN & 0x02) == 0x00) //check of button is still pushed
pin_Value = 1;
}
return pin_Value; //return 1 if pushed- 0 if not pushed
}

## Slide 12
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Interrupts

## Slide 13
Interrupt
time t
mov R1, cent
mov R1, 0x90
mov sensor, R1
ret
mul R1, 9
mov R1, cent
mul R1, 9
div R1, 5
add R1, 32
mov fahr, R1
foreground Thread
background Thread
Fahr = (cent * ) +32
9
5
Interrupt
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
background thread

## Slide 14
Interrupt arrives
Complete current instruction
Save essential register information
Vector to ISR
Save additional register information
Execute body of ISR
Restore other register information
Return from interrupt and restore essential registers
Resume task
Program
Interrupt
time t
mov R1, cent
mul R1, 9
Save
Context
Interrupt Service Routine
Restore
Context
Program
ISR
Interrupt
Latency
Interrupt
Termination
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 15
stack
old R0
old R1
old R2
old R3
old R12
old LR
old PC
old PSR
I
IPSR
BASEPRI
0
0
0
MSP
Thread Mode
Handler Mode
Context Switch
Push Registers
PC = [0x00000048]
Set IPSR = 18
Set LR = 0xFFFFFFF9
Interrupt Context Switch
The steps involved in a context switch from executing the foreground thread (user main program) to switching to the background thread (ISR) when the interrupt occurs
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Main stack pointer
LR = Link Register
PC = Program counter
IPSR = Interrupt Program Status Register
Base Priority Mask register
RAM
Registers
Notes: When the SysTick counter goes from 1 to 0, the Count flag in the NVIC_ST_CTRL_R register is set, triggering an interrupt. The current instruction is finished. (a) Eight registers are pushed on the stack with R0 on top. These registers are pushed onto the stack . (b) The vector address is loaded into the PC (“Vector address” column in Table 12.1). (c) The IPSR register is set to 15 (“Number” column in Table 12.1) (d) The top 24 bits of LR are set to 0xFFFFFF, signifying the processor is executing an ISR. The bottom eight bits specify how to return from interrupt.
BASEPRI special register, which allows you to disable interrupts more selectively. Specifically, you can disable interrupts only with urgency lower than a certain level and leave the higher-urgency interrupts not disabled at all. (This feature is sometimes called “zero interrupt latency”.)
A nested interrupt occurs when a higher priority interrupt suspends an ISR. The lower priority interrupt will finish after the higher priority ISR completes. When one interrupt preempts another, the LR is set to 0xFFFFFFF1, so it knows to return to handler mode. Tail chaining occurs when one ISR executes immediately after another. Optimization occurs because the eight registers need not be popped only to be pushed once again. If an interrupt is triggered and is in the process of stacking registers when a higher priority interrupt is requested, this late arrival interrupt will be executed first.

## Slide 16
stack
RAM
Registers
I
IPSR
BASEPRI
0
0
0
MSP
Thread Mode
Handler Mode
Context Switch
Push Registers
PC = [0x00000048]
Set IPSR = 18
Set LR = 0xFFFFFFF9
Interrupt Context Switch
The steps involved in a context switch from executing the foreground thread (user main program) to switching to the background thread (ISR) when the interrupt occurs
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Main stack pointer
LR = Link Register
PC = Program counter
IPSR = Interrupt Program Status Register
Base Priority Mask register
PC = [0x00000048]
old R0
old R1
old R2
old R3
old R12
old LR
old PC
old PSR
Notes: When the SysTick counter goes from 1 to 0, the Count flag in the NVIC_ST_CTRL_R register is set, triggering an interrupt. The current instruction is finished. (a) Eight registers are pushed on the stack with R0 on top. These registers are pushed onto the stack . (b) The vector address is loaded into the PC (“Vector address” column in Table 12.1). (c) The IPSR register is set to 15 (“Number” column in Table 12.1) (d) The top 24 bits of LR are set to 0xFFFFFF, signifying the processor is executing an ISR. The bottom eight bits specify how to return from interrupt.
BASEPRI special register, which allows you to disable interrupts more selectively. Specifically, you can disable interrupts only with urgency lower than a certain level and leave the higher-urgency interrupts not disabled at all. (This feature is sometimes called “zero interrupt latency”.)
A nested interrupt occurs when a higher priority interrupt suspends an ISR. The lower priority interrupt will finish after the higher priority ISR completes. When one interrupt preempts another, the LR is set to 0xFFFFFFF1, so it knows to return to handler mode. Tail chaining occurs when one ISR executes immediately after another. Optimization occurs because the eight registers need not be popped only to be pushed once again. If an interrupt is triggered and is in the process of stacking registers when a higher priority interrupt is requested, this late arrival interrupt will be executed first.

## Slide 17
stack
RAM
Registers
I
IPSR
BASEPRI
0
0
0
MSP
Thread Mode
Handler Mode
Context Switch
Push Registers
PC = [0x00000048]
Set IPSR = 18
Set LR = 0xFFFFFFF9
Interrupt Context Switch
The steps involved in a context switch from executing the foreground thread (user main program) to switching to the background thread (ISR) when the interrupt occurs
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Main stack pointer
LR = Link Register
PC = Program counter
IPSR = Interrupt Program Status Register
Base Priority Mask register
PC = [0x00000048]
18
old R0
old R1
old R2
old R3
old R12
old LR
old PC
old PSR
Notes: When the SysTick counter goes from 1 to 0, the Count flag in the NVIC_ST_CTRL_R register is set, triggering an interrupt. The current instruction is finished. (a) Eight registers are pushed on the stack with R0 on top. These registers are pushed onto the stack . (b) The vector address is loaded into the PC (“Vector address” column in Table 12.1). (c) The IPSR register is set to 15 (“Number” column in Table 12.1) (d) The top 24 bits of LR are set to 0xFFFFFF, signifying the processor is executing an ISR. The bottom eight bits specify how to return from interrupt.
BASEPRI special register, which allows you to disable interrupts more selectively. Specifically, you can disable interrupts only with urgency lower than a certain level and leave the higher-urgency interrupts not disabled at all. (This feature is sometimes called “zero interrupt latency”.)
A nested interrupt occurs when a higher priority interrupt suspends an ISR. The lower priority interrupt will finish after the higher priority ISR completes. When one interrupt preempts another, the LR is set to 0xFFFFFFF1, so it knows to return to handler mode. Tail chaining occurs when one ISR executes immediately after another. Optimization occurs because the eight registers need not be popped only to be pushed once again. If an interrupt is triggered and is in the process of stacking registers when a higher priority interrupt is requested, this late arrival interrupt will be executed first.

## Slide 18
stack
RAM
Registers
I
IPSR
BASEPRI
0
0
MSP
Thread Mode
Handler Mode
Context Switch
Push Registers
PC = [0x00000048]
Set IPSR = 18
Set LR = 0xFFFFFFF9
Interrupt Context Switch
The steps involved in a context switch from executing the foreground thread (user main program) to switching to the background thread (ISR) when the interrupt occurs
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Main stack pointer
LR = Link Register
PC = Program counter
IPSR = Interrupt Program Status Register
Base Priority Mask register
PC = [0x00000048]
18
LR = 0XFFFFFF9
old R0
old R1
old R2
old R3
old R12
old LR
old PC
old PSR
Notes: When the SysTick counter goes from 1 to 0, the Count flag in the NVIC_ST_CTRL_R register is set, triggering an interrupt. The current instruction is finished. (a) Eight registers are pushed on the stack with R0 on top. These registers are pushed onto the stack . (b) The vector address is loaded into the PC (“Vector address” column in Table 12.1). (c) The IPSR register is set to 15 (“Number” column in Table 12.1) (d) The top 24 bits of LR are set to 0xFFFFFF, signifying the processor is executing an ISR. The bottom eight bits specify how to return from interrupt.
BASEPRI special register, which allows you to disable interrupts more selectively. Specifically, you can disable interrupts only with urgency lower than a certain level and leave the higher-urgency interrupts not disabled at all. (This feature is sometimes called “zero interrupt latency”.)
A nested interrupt occurs when a higher priority interrupt suspends an ISR. The lower priority interrupt will finish after the higher priority ISR completes. When one interrupt preempts another, the LR is set to 0xFFFFFFF1, so it knows to return to handler mode. Tail chaining occurs when one ISR executes immediately after another. Optimization occurs because the eight registers need not be popped only to be pushed once again. If an interrupt is triggered and is in the process of stacking registers when a higher priority interrupt is requested, this late arrival interrupt will be executed first.

## Slide 19
stack
RAM
Registers
I
IPSR
BASEPRI
0
0
MSP
Thread Mode
Handler Mode
Context Switch
Push Registers
PC = [0x00000048]
Set IPSR = 18
Set LR = 0xFFFFFFF9
Interrupt Context Switch
The steps involved in a context switch from executing the foreground thread (user main program) to switching to the background thread (ISR) when the interrupt occurs
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Main stack pointer
LR = Link Register
PC = Program counter
IPSR = Interrupt Program Status Register
Base Priority Mask register
PC = [0x00000048]
18
LR = 0XFFFFFF9
0
old R0
old R1
old R2
old R3
old R12
old LR
old PC
old PSR
Notes: When the SysTick counter goes from 1 to 0, the Count flag in the NVIC_ST_CTRL_R register is set, triggering an interrupt. The current instruction is finished. (a) Eight registers are pushed on the stack with R0 on top. These registers are pushed onto the stack . (b) The vector address is loaded into the PC (“Vector address” column in Table 12.1). (c) The IPSR register is set to 15 (“Number” column in Table 12.1) (d) The top 24 bits of LR are set to 0xFFFFFF, signifying the processor is executing an ISR. The bottom eight bits specify how to return from interrupt.
BASEPRI special register, which allows you to disable interrupts more selectively. Specifically, you can disable interrupts only with urgency lower than a certain level and leave the higher-urgency interrupts not disabled at all. (This feature is sometimes called “zero interrupt latency”.)
A nested interrupt occurs when a higher priority interrupt suspends an ISR. The lower priority interrupt will finish after the higher priority ISR completes. When one interrupt preempts another, the LR is set to 0xFFFFFFF1, so it knows to return to handler mode. Tail chaining occurs when one ISR executes immediately after another. Optimization occurs because the eight registers need not be popped only to be pushed once again. If an interrupt is triggered and is in the process of stacking registers when a higher priority interrupt is requested, this late arrival interrupt will be executed first.

## Slide 20: Nested Vectored Interrupt Controller (NVIC)
Handles exceptions (processor events) and interrupts (external or peripheral events)
8 programmable priority levels (defaults to same level, processed in order of entry in Interrupt Vector Table)
Automatic state saving and restoring: R0–R3, R12, LR, PSR, and PC
Automatic reading of the vector table entry (in parallel to state saving, over Private Peripheral Bus for fast response time)
Pre-emptive/Nested Interrupts with tail-chaining
t
ADC interrupt
Timer_A interrupt
Main application (foreground)
Timer_A interrupt is pending and will execute as soon as ADC finishes (tail chaining)
Notes: The MSP432 Nested Vectored Interrupt Controller, or NVIC, is tightly coupled to the central processing unit. It handles all of the exceptions and interrupts that come into the CPU. There are eight programmable priority levels and priority grouping. In most microcontroller interrupt vector tables, the priority levels for each peripheral are set by the manufacturer, and you have no input into what they are. That's not the case on this device. You can reprogram the priorities as you like.
This device has 7 system level exceptions and 65 peripheral interrupts. It has automatic state save and restore for entering and exiting Interrupt Service Routines, as well as automatic reading of the vector table entry to quickly facilitate this process.
One of the first rules that you learn when programming interrupts on a microcontroller is to not nest interrupts, but sometimes you need to nest the interrupts. For instance, you need to get to a very low latency motor control or device. You need to get to it very quickly, and you have other interrupts that take too long. Those long ISRs will need to be interruptible. On most microcontrollers you will have to program this tedious process in software.
On the MSP432 devices, you can do it by programming the NVIC hardware. You can make interrupts preemptive, and you can nest them. Interrupts can also be tail-chained, which is something I'll explain in the next few slides. Interrupts are deterministic. They're always either 12 cycles or 6 cycles if they're tail-chained.
Taking a look at the diagram at the bottom, we can see this is an application with a two interrupts. From left to the right, the first interrupt that goes off is for motor control. Motor control requires extremely low latency. You can't wait. You must act on the interrupt quickly.
The second interrupt is a repeat of the first.
In the third instance, a communication interrupt like the USCI has started operation. Communication interrupts using involve FIFO’s and buffers, so they can wait. When the motor control interrupt arrives, we can't wait for the communications ISR to complete, the motor control ISR must preempt it.
The remaining instances are further examples. Remember that the nesting behavior is programmed into the NVIC hardware.
Entry
  Automatically pushes registers R0–R3, R12, LR, PSR, and PC onto the stack
  In parallel, ISR is pre-fetched on the instruction bus. ISR ready to start executing as soon as stack PUSH complete
Exit
  Processor state is automatically restored from the stack
  In parallel, interrupted instruction is pre-fetched ready for execution upon completion of stack POP

## Slide 21
Using Interrupts
Interrupts are very useful if there are devices that interface with your program that require a quick response
You should execute as few instructions as possible inside an ISR so other lower priority interrupts are not held off too long.
Use global variable (e.g., Flag) to communicate
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
O
t
h
e
r
c
a
l
c
u
l
a
t
i
o
n
s
1
0
M
a
i
n
p
r
o
g
r
a
m
I
S
R
F
l
a
g
=
0
D
o
i
m
p
o
r
t
a
n
t
s
t
u
f
f
F
l
a
g
F
l
a
g
=
1

## Slide 22
Interrupt Handling
One important component of an ISR is to clear the source of the interrupt.
If the interrupt flag bit is still set when the ISR completes, the code will be re-interrupted and the ISR executes again, and again
However, the interrupt flag bit in the SysTick register is automatically after it’s ISR is executed
Being able to enable and disable all interrupts is useful at certain times (e.g., when timing critical events).
Keep interrupts off while peripherals are being configured so no unexpected interrupts occur before system is ready to handle them.

## Slide 23: Interrupts Declaration on MSP432
The entire Interrupt Vector table is included in the startup file.
Includes reset, hardware and software faults.
Excerpt from file startup_msp432p401r_ccs.c
ISR Handlers:
stubs defined in table. Treated as regular function,
code in user’s application needs to match
void SysTick_Handler (void)
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Reset_Handler, // the reset handler
NMI_Handler, // The NMI handler
HardFault_Handler, // the hard fault handler
MemManage_Handler, // the MPU fault handler
BusFault_Handler, // the bus fault handler
UsageFault_Handler, // the usage fault handler
0, // Reserved
0 , // Reserved
0, // Reserved
0, // Reserved
SVC_Handler, // SVCall handler
DebugMon_Handler, // Debug monitor handler
0, // Reserved
PendSV_Handler, // The PendSV handler
SysTick_Handler, // The SysTick handler
PSS_IRQHandler, // PSS Interrupt
CS_IRQHandler, // CS Interrupt
PCM_IRQHandler, // PCM Interrupt
WDT_A_IRQHandler, // WDT_A Interrupt
FPU_IRQHandler, // FPU Interrupt
FLCTL_IRQHandler, // Flash Controller Interrupt
COMP_E0_IRQHandler, // COMP_E0 Interrupt
COMP_E1_IRQHandler, // COMP_E1 Interrupt
TA0_0_IRQHandler, // TA0_0 Interrupt
TA0_N_IRQHandler, // TA0_N Interrupt
TA1_0_IRQHandler, // TA1_0 Interrupt
#pragma RETAIN(interruptVectors)
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors [ ])(void) =
{
(void (*)(void))((uint32_t) & __STACK_END),
/* The initial stack pointer */

## Slide 24: SysTick Timer
Timer/Counter operation
  24-bit counter
    decrements at bus clock frequency
    With 3MHz bus clock, decrements every 333.3 ns
  Counting is from n  0
  Flag is set (and interrupt generated if enabled) when count goes from 1  0
Notes: Modulo (mod or %) operation gives the remainder: (a mod n) is the remainder when a is divided by n.
When a < n, (a mod n) is simply a.
When current_value reaches 0, then the next value is [(0-1)mod (n+1)] = -1 mod (n+1) = n
That is the counter gets reset to max value n after it reaches 0.

## Slide 25: SysTick Timer
Initialization (4 steps)
      CLK_SRC = 1 (bus clock is the only option)
      INTEN = 0 for no interrupts
      ENABLE = 1 to enable
SysTick -> CTRL (Control Status Register STCSR)
SysTick -> LOAD (Reload Value Register STRVR)
SysTick -> VAL (Current Value Register STCVR)
Address
31
-
24
23
-
17
16
15
-
3
2
1
0
Name
0x
E000E010
0
0
C
OUNT
0
CLK_SRC
INTEN
ENABLE
SYSTICK_STCSR
0x
E000E014
0
24
-
bit RELOAD value
SYSTICK_STRVR
0x
E000E018
0
24
-
bit CURRENT value of
SysTick counter
SYSTICK_STCVR
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Notes: RELOAD value is the value to load into the counter (reset) every time it hits zero, i.e. the n value from the previous slide

## Slide 26: Using the SysTick Timer
What limits the delay to 5.592 s?
How could you make a longer delay?
void SysTick_Init (void)
{ //initialization of systic timer
SysTick -> CTRL = 0; // disable SysTick During step
SysTick -> LOAD = 0x00FFFFFF; // max reload value
SysTick -> VAL = 0; // any write to current clears it
SysTick -> CTRL = 0x00000005; // enable systic, 3MHz, No Interrupts
}
void SysTick_delay (uint16_t delay)
{ // Systick delay function
SysTick -> LOAD = ((delay * 3000) - 1); //delay for 1 msecond per delay value
SysTick -> VAL = 0; // any write to CVR clears it
while ( (SysTick - > CTRL & 0x00010000) == 0); // wait for flag to be SET
}
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 27: Using the SysTick Timer
void SysTick_Init_interrupt (void)
{ //initialization of systic timer
SysTick -> CTRL = 0; // disable SysTick During step
SysTick -> LOAD = 3000; // reload value for 1ms interrupts
SysTick -> VAL = 0; // any write to current clears it
SysTick -> CTRL = 0x00000007; // enable SysTick, 3MHz, with Interrupts
}
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
// ---- interrupt service routine for SysTick timer
void SysTick_Handler (void)
{
timeout = 1 ; // set flag for timeout of SysTick, rest in main
intervalCnt++ ; // increment interval timer by 1ms, reset in main ( )
}
__enable_irq(); // enable global interrupts
Remember to declare global variables and use the volatile keyword
How could you make these interrupts happen every 10 ms?

## Slide 28
Interrupt Handling
One important component of an ISR is to clear the source of the interrupt.
If, for example, the interrupt flag bit is set when the ISR completes, the code will be re-interrupted and the ISR executes again, and again
However, the interrupt flag bit in the SysTick register is automatically cleared whenever it generates an interrupt and the ISR is executed
.
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 29: Example SysTick Timer
void SysTick_Init_interrupt (void) { //initialization of systic timer
SysTick -> CTRL = 0; // disable SysTick During step
SysTick -> LOAD = 1500000; // reload value for 0.5s interrupts
SysTick -> VAL = 0; // any write to current clears it
SysTick -> CTRL = 0x00000007; // enable systic, 3MHz, Interrupts
}
void SysTick_Handler (void) {
timeout = 1 ; // set flag for timeout of SysTick, rest in main
}
volatile uint32_t timeout ;
int main(void)
{
WDT_A->CTL = WDT_A_CTL_PW | WDT_A_CTL_HOLD; // Halting the Watchdog
P2->SEL0 &=~ BIT4 ; // Set pin 4 GPIO
P2->SEL1 &=~ BIT4 ; // Set pin 4 GPIO
P2->DIR |= BIT4 ; // Set pin 4 OUTPUT
SysTick_Init_interrupt ( ); // initialize systic with interrupt
__enable_irq ( ); // enable global interrupts
while (1)
{
if ( timeout )
{
P2->OUT ^= BIT4; // Toggle pin 4 every second
timeout = 0;
}
}
}
Toggle pin 4 PORT 2 every 1 second
Using SysTick and interrupts

## Slide 30: interrupts
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 31
Interrupts vectors
startup_msp432p401r_ccs.c
ADC14_IRQHandler // ADC14 Interrupt
T32_INT1_IRQHandler // T32_INT1 Interrupt
T32_INT2_IRQHandler // T32_INT2 Interrupt
T32_INTC_IRQHandler // T32_INTC Interrupt
AES256_IRQHandler // AES256 Interrupt
RTC_C_IRQHandler // RTC_C Interrupt
DMA_ERR_IRQHandler // DMA_ERR Interrupt
DMA_INT3_IRQHandler // DMA_INT3 Interrupt
DMA_INT2_IRQHandler // DMA_INT2 Interrupt
DMA_INT1_IRQHandler // DMA_INT1 Interrupt
DMA_INT0_IRQHandler // DMA_INT0 Interrupt
PORT1_IRQHandler // Port1 Interrupt
PORT2_IRQHandler // Port2 Interrupt
PORT3_IRQHandler // Port3 Interrupt
PORT4_IRQHandler // Port4 Interrupt
PORT5_IRQHandler // Port5 Interrupt
PORT6_IRQHandler // Port6 Interrupt
EUSCIA0_IRQHandler // EUSCIA0 Interrupt
EUSCIA1_IRQHandler // EUSCIA1 Interrupt
EUSCIA2_IRQHandler, EUSCIA2 Interrupt
EUSCIA3_IRQHandler // EUSCIA3 Interrupt
EUSCIB0_IRQHandler // EUSCIB0 Interrupt
EUSCIB1_IRQHandler, // EUSCIB1 Interrupt
EUSCIB2_IRQHandler // EUSCIB2 Interrupt
EUSCIB3_IRQHandler, // EUSCIB3 Interrupt
Reset_Handler, // the reset handler
NMI_Handler, // The NMI handler
HardFault_Handler // the hard fault handler
MemManage_Handler // the MPU fault handler
BusFault_Handler // the bus fault handler
UsageFault_Handler, // the usage fault handler
0, // Reserved
0 , // Reserved
0 // Reserved
0, // Reserved
SVC_Handler, // SVCall handler
DebugMon_Handler, // Debug monitor handler
0 // Reserved
SysTick_Handler, // The SysTick handler
PSS_IRQHandler, // PSS Interrupt
CS_IRQHandler, // CS Interrupt
PCM_IRQHandler, // PCM Interrupt
WDT_A_IRQHandler, // WDT_A Interrupt
FPU_IRQHandler // FPU Interrupt
FLCTL_IRQHandler, // Flash Controller Interrupt
COMP_E0_IRQHandler, // COMP_E0 Interrupt
COMP_E1_IRQHandler // COMP_E1 Interrupt
TA0_0_IRQHandler // TA0_0 Interrupt
TA0_N_IRQHandler, // TA0_N Interrupt
TA1_0_IRQHandler // TA1_0 Interrupt
TA1_N_IRQHandler // TA1_N Interrupt
TA2_0_IRQHandler // TA2_0 Interrupt
TA2_N_IRQHandler // TA2_N Interrupt
TA3_0_IRQHandler // TA3_0 Interrupt
TA3_N_IRQHandler // TA3_N Interrupt
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 32
Interrupts vectors
ISER0 Register Irq 0 to 31 Set Enable Register.
Use the Interrupt Set-Enable Registers to enable interrupts & determine which interrupts are currently enabled.
Figure 2-20. ISER0 Register
ISER1 Register Irq 32 to 63 Set Enable Register.
Use the Interrupt Set-Enable Registers to enable interrupts & determine which interrupts are currently enabled.
Figure 2-21. ISER1 Register
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 33
Figure 2-20.
ISER0 Register
To enable the interrupt vectors from 0-31
use ISER0 register
NVIC->ISER[0] = 1 << ( (ADC14_IRQn) & 31);
NVIC->ISER[0] = 1 << 24;
NVIC->ISER[0] = 1 << ( (TA0_0_IRQn) & 31);
NVIC->ISER[0] = 1 << 8;
Or
NVIC_EnableIRQ (TA0_N_IRQn);
NVIC_EnableIRQ (ADC14_IRQn);
PSS_IRQn = 0, PSS Interrupt
CS_IRQn = 1, CS Interrupt
PCM_IRQn = 2, PCM Interrupt
WDT_A_IRQn = 3, WDT_A Interrupt
FPU_IRQn = 4, FPU Interrupt
FLCTL_IRQn = 5, Flash Interrupt
COMP_E0_IRQn = 6, COMP_E0 Interrupt
COMP_E1_IRQn = 7, COMP_E1 Interrupt
TA0_0_IRQn = 8, TA0_0 Interrupt
TA0_N_IRQn = 9, TA0_N Interrupt
TA1_0_IRQn = 10, TA1_0 Interrupt
TA1_N_IRQn = 11, TA1_N Interrupt
TA2_0_IRQn = 12, TA2_0 Interrupt
TA2_N_IRQn = 13, TA2_N Interrupt
TA3_0_IRQn = 14, TA3_0 Interrupt
TA3_N_IRQn = 15, TA3_N Interrupt
EUSCIA0_IRQn = 16, EUSCIA0 Interrupt
EUSCIA1_IRQn = 17, EUSCIA1 Interrupt
EUSCIA2_IRQn = 18, EUSCIA2 Interrupt
EUSCIA3_IRQn = 19, EUSCIA3 Interrupt
EUSCIB0_IRQn = 20, EUSCIB0 Interrupt
EUSCIB1_IRQn = 21, EUSCIB1 Interrupt
EUSCIB2_IRQn = 22, EUSCIB2 Interrupt
EUSCIB3_IRQn = 23, EUSCIB3 Interrupt
ADC14_IRQn = 24, ADC14 Interrupt
T32_INT1_IRQn = 25, T32_INT1 Interrupt
// Enable all interrupts for MSP432
// declare before the while loop
__enable_interrupt ( );

## Slide 34
Figure 2-20.
ISER1 Register
To enable the interrupt vectors from 0-31
use ISER1 register
NVIC->ISER[1] = 1 << ( (PORT1_IRQn) & 31);
NVIC->ISER[1] = 1 << 35-32;
Or
NVIC_EnableIRQ (PORT1_IRQn);
// Enable all interrupts for MSP432
// declare before the while loop
__enable_interrupt ( );
T32_INT2_IRQn = 26, T32_INT2 Interrupt
T32_INTC_IRQn = 27, T32_INTC Interrupt
AES256_IRQn = 28, AES256 Interrupt
RTC_C_IRQn = 29, RTC_C Interrupt
DMA_ERR_IRQn = 30, DMA_ERR Interrupt
DMA_INT3_IRQn = 31, DMA_INT3 Interrupt
DMA_INT2_IRQn = 32, DMA_INT2 Interrupt
DMA_INT1_IRQn = 33, DMA_INT1 Interrupt
DMA_INT0_IRQn = 34, DMA_INT0 Interrupt
PORT1_IRQn = 35, Port1 Interrupt
PORT2_IRQn = 36, Port2 Interrupt
PORT3_IRQn = 37, Port3 Interrupt
PORT4_IRQn = 38, Port4 Interrupt
PORT5_IRQn = 39, Port5 Interrupt
RTC_C_IRQn = 40 Port6 Interrupt
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 35: P0RTx interrupts
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 36
PxIES Register
Port X Interrupt Edge Select Register (X = 1, 2, 3, 4, 5, 6, 7, 8, 9 or 10)
PxIE Register
Port X Interrupt Enable Register (X = 1, 2, 3, 4, 5, 6, 7, 8, 9 or 10)
Figure 10-10
PxIES Register
Figure 10-11
PxIE Register
Example
P1->IES |= 0x11; //Set pin interrupt to trigger when it goes from high to low
Example
P1 -> IE |= 0x11; // Set interrupt on for p1.1 and 1.4
PxIFG Register
Port X Interrupt Flag Register (X = 1, 2, 3, 4, 5, 6, 7, 8, 9 or 10)
If ( P1->IFG & BIT1)
P1->OUT ^= BIT0; // Toggle the LED
P1->IFG &= ~BIT1; // always clear the flag before you exit the interrupt ISR
Figure 10-12
PxIFG Register

## Slide 37
P1.1 is configured as an input. Pressing the button P1.1 service an interrupt service routine ISR results in toggling an LED on PORT3 pin5 in device waking up and servicing the Port1 ISR.
MCLK = SMCLK = 3MHz
void Port1_init (void);
{
P1->SEL0 &=~ BIT1;
P1->SEL1 &=~ BIT1;
P1->DIR &=~ BIT1;
P1->REN | = BIT1; // Enable Internal resistor
P1->OUT | = BIT1; // Enable pull-up resistor (P1.1 output high)
P1->IES | = BIT1; //Set pin interrupt to trigger when it goes from high to low
P1->IE | = BIT1; // Enable interrupt for P1.1
P1->IFG = 0; // Clear all P1 interrupt flags
}
void Port3_init (void)
{
P3->SEL0 &=~ BIT5; // Set P3.5 GPIO
P3->SEL1 &=~ BIT5; // Set P3.5 GPIO
P3->DIR |= BIT5; // set P3.5 as an output
}
void PORT1_IRQHandler(void) // Port1 ISR
{
If ( P1->IFG & BIT1 ) // If P1.1 had an interrupt (going from high to low
P3->OUT ^= BIT5; // Toggling the output on the LED
P1->IFG &= ~BIT1; // Reset the interrupt flag
}
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 38
#include "msp.h"
int main(void)
{
WDT_A->CTL = WDT_A_CTL_PW | WDT_A_CTL_HOLD; // Hold the watchdog
Port1_init ( );
Port3_init ( );
NVIC->ISER[1] = 1 << ((PORT1_IRQn) & 31); // Enable Port 1 interrupt on the NVIC
__enable_interrupt ( ); // Enable global interrupt
while ( 1 )
{
; // Hardware is doing all the work, so nothing more to do in this while loop.
}
}
P1.1 is configured as an input. Pressing the button P1.1 service an interrupt service routine ISR results in toggling an LED on PORT3 pin5 in device waking up and servicing the Port1 ISR.
MCLK = SMCLK = 3MHz
Dr. Nabeeh Kandalaft EGR226 Grand valley State University