## Slide 1
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Introduction to Digital Systems
EGR 226
Lecture_9

## Slide 2: Topic for today’s lecture
write C code to control pixels on an LCD matrix display
describe the concept of structured design
describe Unified Markup Language tools developed for system design
produce a UML state diagram to describe your project design concept
produce a specifications requirements document
begin work on your embedded system design document
Dr. Nabeeh Kandalaft EGR226 Grand valley State University

## Slide 3: The ST7735R TFT LCD Controller/Driver
From: ST7735R single-chip controller/driver data sheet
Notes: Look up table

## Slide 4: The ST7735R TFT LCD Controller/Driver

## Slide 5
// Configure Flash wait-state to 1 for both banks 0 & 1
FLCTL->BANK0_RDCTL = (FLCTL->BANK0_RDCTL & ~(FLCTL_BANK0_RDCTL_WAIT_MASK)) |
FLCTL_BANK0_RDCTL_WAIT_1;
FLCTL->BANK1_RDCTL = (FLCTL->BANK0_RDCTL & ~(FLCTL_BANK0_RDCTL_WAIT_MASK)) |
FLCTL_BANK1_RDCTL_WAIT_1;
//Configure HFXT to use 48MHz crystal, source to MCLK & HSMCLK*
PJ->SEL0 |= BIT2 | BIT3; // Configure PJ.2/3 for HFXT function
PJ->SEL1 &= ~(BIT2 | BIT3);
CS->KEY = CS_KEY_VAL ; // Unlock CS module for register access
CS->CTL2 |= CS_CTL2_HFXT_EN | CS_CTL2_HFXTFREQ_6 | CS_CTL2_HFXTDRIVE;
while(CS->IFG & CS_IFG_HFXTIFG)
CS->CLRIFG |= CS_CLRIFG_CLR_HFXTIFG;
/* Select MCLK & HSMCLK = HFXT, no divider */
CS->CTL1 = CS->CTL1 & ~(CS_CTL1_SELM_MASK | CS_CTL1_DIVM_MASK | CS_CTL1_SELS_MASK | CS_CTL1_DIVHS_MASK) | CS_CTL1_SELM__HFXTCLK | CS_CTL1_SELS__HFXTCLK;
CS->KEY = 0; // Lock CS module from unintended accesses
Set Clock Module To Use External 48 MHz Crystal

## Slide 6: Check Clock Signals After Setting in CS Module
After setting the clock signals, especially after setting up an external crystal oscillator verify that the clocks were set correctly
HINT: YOU can find it on Port 4 alternate functions

## Slide 7
P1.0, P1.2, P1.3, P2.0, P2.1, P2.2,
P3.1, & P3.4 are available on jumpers,
P1.1, P1.4, P8.1 are not)
MSP432
Architecture
General-Purpose I/O (GPIO):
78 pins
10 ports
Pins are multiplexed between
std I/O and peripherals
Only 67 pins are available
G
P
I
O
P
o
r
t
3
e
U
S
C
I
P
1
.
7
/
U
C
B
0
S
C
L
P
1
.
6
/
U
C
B
0
S
D
A
P
1
.
5
/
U
C
B
0
C
L
K
P
1
.
4
/
U
C
B
0
S
T
E
P
1
.
3
/
U
C
A
0
T
X
D
P
1
.
2
/
U
C
A
0
R
X
D
P
1
.
1
/
U
C
A
0
C
L
K
P
1
.
0
/
U
C
A
0
S
T
E
P
2
.
7
/
T
A
0
.
4
P
2
.
6
/
T
A
0
.
3
P
2
.
5
/
T
A
0
.
2
P
2
.
4
/
T
A
0
.
1
P
2
.
3
/
U
C
A
1
T
X
D
P
2
.
2
/
U
C
A
1
R
X
D
P
2
.
1
/
U
C
A
1
C
L
K
P
2
.
0
/
U
C
A
1
S
T
E
P
3
.
7
/
U
C
B
2
S
C
L
P
3
.
6
/
U
C
B
2
S
D
A
P
3
.
5
/
U
C
B
2
C
L
K
P
3
.
4
/
U
C
B
2
S
T
E
P
3
.
3
/
U
C
A
2
T
X
D
P
3
.
2
/
U
C
A
2
R
X
D
P
3
.
1
/
U
C
A
2
C
L
K
P
3
.
0
/
U
C
A
2
S
T
E
P
4
.
7
/
A
6
P
4
.
6
/
A
7
P
4
.
5
/
A
8
P
4
.
4
/
A
9
P
4
.
3
/
R
T
C
C
L
K
/
A
1
0
P
4
.
2
/
T
A
2
C
L
K
/
A
1
1
P
4
.
1
/
A
1
2
P
4
.
0
/
A
1
3
P
5
.
7
/
T
A
2
.
2
P
5
.
6
/
T
A
2
.
1
P
5
.
5
/
A
0
P
5
.
4
/
A
1
P
5
.
3
/
A
2
P
5
.
2
/
A
3
P
5
.
1
/
A
4
P
5
.
0
/
A
5
e
U
S
C
I
P
6
.
7
/
T
A
2
.
4
/
/
U
C
B
3
S
C
L
P
6
.
6
/
T
A
2
.
3
/
U
C
B
3
S
D
A
P
6
.
5
/
U
C
B
1
S
C
L
P
6
.
4
/
U
C
B
1
S
D
A
P
6
.
3
/
U
C
B
1
C
L
K
P
6
.
2
/
U
C
B
1
S
T
E
P
6
.
1
/
A
1
4
P
6
.
0
/
A
1
5
P
7
.
7
/
T
A
1
.
1
/
C
0
.
2
P
7
.
6
/
T
A
1
.
2
/
C
0
.
3
P
7
.
5
/
T
A
1
.
3
/
C
0
.
4
P
7
.
4
/
T
A
1
.
4
/
C
0
.
5
P
7
.
3
/
T
A
0
.
0
P
7
.
2
/
C
1
O
U
T
/
T
A
1
C
L
K
P
7
.
1
/
C
0
O
U
T
/
T
A
0
C
L
K
P
7
.
0
/
S
M
C
L
K
/
D
M
A
E
0
P
8
.
7
/
A
1
8
P
8
.
6
/
A
1
9
P
8
.
5
/
A
2
0
P
8
.
4
/
A
2
1
P
8
.
3
/
T
A
3
C
L
K
/
A
2
2
P
8
.
2
/
T
A
3
.
2
/
A
2
3
P
8
.
1
/
U
C
B
3
C
L
K
/
T
A
2
.
0
P
8
.
0
/
U
C
B
3
S
T
E
/
T
A
1
.
0
P
9
.
7
/
U
C
A
3
T
X
D
P
9
.
6
/
U
C
A
3
R
X
D
P
9
.
5
/
U
C
A
3
C
L
K
P
9
.
4
/
U
C
A
3
S
T
E
P
9
.
3
/
T
A
3
.
4
P
9
.
2
/
T
A
3
.
3
P
9
.
1
/
A
1
6
P
9
.
0
/
A
1
7
P
1
0
.
5
/
T
A
3
.
1
/
C
0
.
6
P
1
0
.
4
/
T
A
3
.
0
/
C
0
.
7
P
1
0
.
3
/
U
C
B
3
S
C
L
P
1
0
.
2
/
U
C
B
3
S
D
A
P
1
0
.
1
/
U
C
B
3
C
L
K
P
1
0
.
0
/
U
C
B
3
S
T
E
C
o
r
t
e
x
M
4
S
y
s
t
i
c
k
N
V
I
C
P
e
r
i
p
h
e
r
a
l
B
u
s
T
i
m
e
r
A
S
y
s
t
e
m
B
u
s
I
n
t
e
r
f
a
c
e
G
P
I
O
P
o
r
t
1
e
U
S
C
I
G
P
I
O
P
o
r
t
5
A
D
C
1
4
G
P
I
O
P
o
r
t
2
G
P
I
O
P
o
r
t
4
A
D
C
1
4
T
i
m
e
r
A
G
P
I
O
P
o
r
t
6
A
D
C
1
4
T
i
m
e
r
A
e
U
S
C
I
G
P
I
O
P
o
r
t
7
T
i
m
e
r
A
G
P
I
O
P
o
r
t
8
A
D
C
1
4
e
U
S
C
I
G
P
I
O
P
o
r
t
9
A
D
C
1
4
e
U
S
C
I
G
P
I
O
P
o
r
t
1
0
T
i
m
e
r
A
e
U
S
C
I
T
i
m
e
r
A
T
i
m
e
r
A
T
i
m
e
r32
R
T
C
Almost 32
ADC Channels

## Slide 8: Partial Table of Alternate Pin Functions
Pin | PxSEL1=0, PxSEL0=0 | PxSEL1=0, PxSEL0=1 | PxSEL1=1, PxSEL0=0 | PxSEL1=1, PxSEL0=1
P1.0 | Port | UCA0STE |  | 
P1.1 | Port | UCA0CLK |  | 
P1.2 | Port | UCA0RXD/UCA0SOMI |  | 
P1.3 | Port | UCA0TXD/UCA0SIMO |  | 
P1.4 | Port | UCB0STE |  | 
P1.5 | Port | UCB0CLK |  | 
P1.6 | Port | UCB0SIMO/UCB0SDA |  | 
P1.7 | Port | UCB0SOMI/UCB0SCL |  | 
P2.0 | Port | UCA1STE |  | 
P2.1 | Port | UCA1CLK |  | 
P2.2 | Port | UCA1RXD/UCA1SOMI |  | 
P2.3 | Port | UCA1TXD/UCA1SIMO |  | 
P2.4 | Port | TA0.CCI1Aa / TA0.1b |  | 
P2.5 | Port | TA0.CCI2Aa / TA0.2b |  | 
P2.6 | Port | TA0.CCI3Aa / TA0.3b |  | 
P2.7 | Port | TA0.CCI4Aa / TA0.4b |  | 
P3.0 | Port | UCA2STE |  | 
P3.1 | Port | UCA2CLK |  | 
P3.2 | Port | UCA2RXD/UCA2SOMI |  | 
P3.3 | Port | UCA2TXD/UCA2SIMO |  | 
P3.4 | Port | UCB2STE |  | 
P3.5 | Port | UCB2CLK |  | 
P3.6 | Port | UCB2SIMO/UCB2SDA |  | 
P3.7 | Port | UCB2SOMI/UCB2SCL |  | 
P4.0 | Port |  |  | A13
P4.1 | Port |  |  | A12
P4.2 | Port | ACLKb | TA2CLKa | A11
P4.3 | Port | MCLKb | RTCCLKb | A10
P4.4 | Port | HSMCLKb | SVMHOUTb | A9
P4.5 | Port |  |  | A8
P4.6 | Port |  |  | A7
P4.7 | Port |  |  | A6
SEL1 and SEL0 bits on the MSP432 specify alternate functions.
P1.2 and P1.3 are hardwired to the serial port to USB interface.
Table 4.1 in Valvano’s textbook
Default Primary Secondary Tertiary
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
General Purpose I/O
Primary Module Function
Secondary Module Function
Tertiary Module Function
0
1
2
3
MUX bits of
PxSEL0 & PxSEL1
Pin of Chip

## Slide 9: Check Clock Signals After Setting in CS Module
After setting the clock signals, especially after setting up an external crystal oscillator verify that the clocks were set correctly
/* Step 4: Output MCLK to port pin to demonstrate 48MHz operation */
P4->DIR |= BIT3 | BIT4;
P4->SEL0 |= BIT3 | BIT4; // Output MCLK
P4->SEL1 &= ~ (BIT3 | BIT4);

## Slide 10: MSP432 eUSCI in SPI mode
This flexible hardware module can be configured to serve multiple purposes (serial, I2C, SPI)
SPI drivers monitor RXIFG and TXIFG to know when to read and write to buffers
from TI MSP432P4XX Family Techncal Reference Guide
Clock polarity and edge timing must be set properly to match slave device

## Slide 11: Basic Master Mode SPI C Code
From ST7735.c, Adafruit library modified by Daniel Valvano (in the archive you can download from
http://edx-org-utaustinx.s3.amazonaws.com/UT601x/ValvanoWare.zip )
// ST7735.c
// Runs on MSP432
// Low level drivers for the ST7735 160x128 LCD
// Backlight (pin 10) connected to +3.3 V  pin 8, has a small series resistor
// MISO (pin 9) unconnected
// SCK (pin 8) connected to P9.5 (UCA3CLK)  pin 7
// MOSI (pin 7) connected to P9.7 (UCA3SIMO)  pin 6 *** labeled SDA ***
// TFT_CS (pin 6) connected to P9.4 (UCA3STE) pin 3 labeled CS
// CARD_CS (pin 5) unconnected
// Data/Command (pin 4) connected to P9.2 (GPIO), high for data, low for command
 pin 5 *** labeled A0 ***
// RESET (pin 3) connected to P9.3 (GPIO)  pin 4
// VCC (pin 2) connected to +3.3 V  pin 1 *** be very careful not to switch VCC and GND !!!
// Gnd (pin 1) connected to ground  pin 2
The example code we’re suggesting you start with was written for a different implementation of a ST7735 module, therefore, there are some pin location and name differences.

## Slide 12: C code to control pixels on an LCD matrix display
From ST7735.c, Adafruit library modified by Daniel Valvano
// toggle RST low to reset; CS low so it'll listen to us
// UCA3STE is temporarily used as GPIO
P9->SEL0 &= ~0x1C;
P9->SEL1 &= ~0x1C; // configure P9.2 (D/C), P9.3 (Reset), and P9.4 (TFT_CS) as GPIO
P9->DIR |= 0x1C; // make P9.2 (D/C), P9.3 (Reset), and P9.4 (TFT_CS) out
TFT_CS &=~ TFT_CS_BIT;
RESET |= RESET_BIT;
Delay1ms(500);
RESET &=~ RESET_BIT;
Delay1ms(500);
RESET |= RESET_BIT;
Delay1ms(500);
Commands for initializing the controller

## Slide 13: C code to control pixels on an LCD matrix display
From ST7735.c, Adafruit library modified by Daniel Valvano
// initialize Eusci
EUSCI_A3->CTLW0 = 0x0001; // hold the eUSCI module in reset mode
// configure EUSCI_A3->CTLW0 for:
// bit15 EUSCI_A_CTLW0_CKPH = 1; data shifts in on first edge, out on following edge
// bit14 EUSCI_A_CTLW0_CKPL = 0; clock is low when inactive
// bit13 EUSCI_B_CTLW0_MSB = 1; MSB first
// bit12 EUSCI_B_CTLW0_SEVENBIT = 0; 8-bit data
// bit11 EUSCI_B_CTLW0_MST = 1; master mode
// bits10-9 UCMODEx = 2; UCSTE active low
// bit8 EUSCI_B_CTLW0_SYNC = 1; synchronous mode
// bits7-6 UCSSELx = 2; eUSCI clock SMCLK
// bits5-2 reserved
// bit1 EUSCI_B_CTLW0_STEM = 1; UCSTE pin enables slave
// bit0 EUSCI_A_CTLW0_SWRST = 1; reset enabled
EUSCI_A3->CTLW0 = 0xAD83;
Commands for initializing the eUSCI module in SPI mode

## Slide 14: C code to control pixels on an LCD matrix display
From ST7735.c, Adafruit library modified by Daniel Valvano
// set the baud rate for the eUSCI which gets its clock from SMCLK
// Clock_Init48MHz() from ClockSystem.c sets SMCLK = HFXTCLK/4 = 12 MHz
// if the SMCLK is set to 12 MHz, divide by 3 for 4 MHz baud clock
EUSCI_A3->BRW = 3;
// modulation is not used in SPI mode, so clear EUSCI_A3->MCTLW
EUSCI_A3->MCTLW = 0;
P9->SEL0 |= 0xB0;
P9->SEL1 &= ~0xB0; // configure P9.7, P9.5, and P9.4 as primary module function
P9->SEL0 &= ~0x0C;
P9->SEL1 &= ~0x0C; //configure P9.3 and P9.2 as GPIO (Reset and D/C pins)
P9->DIR |= 0x0C; // make P9.3 and P9.2 out (Reset and D/C pins)
EUSCI_A3->CTLW0 &= ~0x0001; // enable eUSCI module
EUSCI_A3->IE &= ~0x0003; // disable interrupts
Commands for initializing the eUSCI module in SPI mode (con’t)

## Slide 15: C code to control pixels on an LCD matrix display
// This is a helper function that sends an 8-bit command to the LCD.
// Inputs: c 8-bit code to transmit
// Outputs: 8-bit reply
// Assumes: UCA3 and Port 9 have already been initialized and enabled
uint8_t static writecommand(uint8_t c) {
while((EUSCI_A3->IFG & 0x0002)==0x0000){}; // wait until EUSCI_A3->TXBUF empty
DC &= ~DC_BIT;
EUSCI_A3->TXBUF = c; // command out
while((EUSCI_A3->IFG &0x0001)==0x0000){}; // wait until EUSCI_A3->RXBUF full
return EUSCI_A3->RXBUF; // return the response
}
// This is a helper function that sends a piece of 8-bit data to the LCD.
// Inputs: c 8-bit data to transmit
// Outputs: 8-bit reply
// Assumes: UCA3 and Port 9 have already been initialized and enabled
uint8_t static writedata(uint8_t c) {
while((EUSCI_A3->IFG & 0x0002)==0x0000){}; //wait until EUSCI_A3->TXBUF empty
DC |= DC_BIT;
EUSCI_A3->TXBUF = c; // data out
while((EUSCI_A3->IFG & 0x0001)==0x0000){}; // wait until EUSCI_A3->RXBUF full
return EUSCI_A3->RXBUF; // return the response
}
From ST7735.c, Adafruit library modified by Daniel Valvano

## Slide 16: Code to set up the ST7735 LCD Controller
static const uint8_t
Bcmd[] = { // Initialization commands for 7735B screens
18, // 18 commands in list:
ST7735_SWRESET, DELAY, // 1: Software reset, no args, w/delay
50, // 50 ms delay
ST7735_SLPOUT , DELAY, // 2: Out of sleep mode, no args, w/delay
255, // 255 = 500 ms delay
ST7735_COLMOD , 1+DELAY, // 3: Set color mode, 1 arg + delay:
0x05, // 16-bit color
10, // 10 ms delay
ST7735_FRMCTR1, 3+DELAY, // 4: Frame rate control, 3 args + delay:
0x00, // fastest refresh
0x06, // 6 lines front porch
0x03, // 3 lines back porch
10, // 10 ms delay
ST7735_MADCTL , 1 , // 5: Memory access ctrl (directions), 1 arg:
0x08, // Row addr/col addr, bottom to top refresh
ST7735_DISSET5, 2 , // 6: Display settings #5, 2 args, no delay:
0x15, // 1 clk cycle nonoverlap, 2 cycle gate
// rise, 3 cycle osc equalize
0x02, // Fix on VTL
ST7735_INVCTR , 1 , // 7: Display inversion control, 1 arg:
0x0, // Line inversion
⁞
From ST7735.c, Adafruit library modified by Daniel Valvano
Excerpt from commands for initializing the controller

## Slide 17: Embedded Systems Design
When approaching embedded systems architecture design, several models can be applied to describe the design cycle.
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
The big-bang model:
there is essentially no planning or processes in place before and during
the development of a system.
The code-and-fix model:
product requirements are defined but no processes are in place
before the start of development.
The waterfall model:
there is a process for developing a system in steps, where results
of one step flow into the next step.
The spiral model:
there is a process for developing a system in steps, and throughout the various steps, feedback is obtained and incorporated back into the process.

## Slide 18: Structured Design
Dr. Nabeeh Kandalaft EGR226 Grand valley State University
Hardware
Implementation
Hardware
Testing
Hardware
Design
System
Integration
System
Validation
System
Architecture
Specification
Requirements
Analysis
Requirements Document
Functional Specification
Hardware Architecture
Specification
Block Diagram
Schematics,
Prototypes
Verified Hardware
Verified System
(does it work as designed?)
Validated System
(does it meet all requirements?)
Software
Implementation
Software
Testing
Software
Design
Software Architecture
Specification
Module
Specification
Modules
Coded
Verified Software

## Slide 19: The System Requirements Specification (SyRS)
IEEE guidelines:
distinction between the system requirements (what the system must do, the SyRS) and process requirements (how to construct the system, the design document)
the SyRS provides a ‘black-box’ description of what the system must do, in terms of the system’s interactions or interfaces with its external environment.
the SyRS completely describes all inputs, outputs, and required relationships between inputs and outputs.
“a well-formed requirement is a statement of system functionality (a capability) that can be validated, that must be met or possessed by a system to solve a customer problem , and that is qualified by measurable conditions and bounded by constraints.”
from: IEEE Guide for Developing System Requirements Specifications, IEEE Std 1233, 1998 Edition

## Slide 20: The SYstem Requirements Specification
Each requirement (numbered e.g., Req. 1) must possess the following properties:
a) Abstract. Each requirement must be implementation independent.
b) Unambiguous. Each requirement must be stated in such a way so that it can be interpreted in only one way.
c) Traceable. For each requirement it must be feasible to determine a relationship between specific documented customer statement(s) of need and the specific statements in the definition of the system given in the SyRS.
d) Verifiable Each requirement must have the means to prove that the system satisfies the requirements.
from: IEEE Guide for Developing System Requirements Specifications, IEEE Std 1233, 1998 Edition

## Slide 21: Verification vs Validation
Validation: DONE FIRST!
  Does your specification meet customer intent
Verification
  Does your product meet the requirement
    Test
    Inspection
    Analyze

## Slide 22: The SYstem Requirements Specification
What you need to do:
Review the project description document
Get with your partner and decide what your design must accomplish
  The core requirements use the key word “must”*, the extra features use the key word “may”
  Number the requirements
Write the System Requirements Specification document with the following parts:
  Introduction with purpose and goals of your embedded system
  A block diagram showing the major components
  A “walk through” of the user interface
  A list of requirements written as described in the previous slide
  A verification and validation plan
  A timeline for the project with weekly milestones
*For an interesting discussion of legal terminiology, see http://www.faa.gov/about/initiatives/plain_language/articles/mandatory/

## Slide 23: Developing a System Architecture
Describing an embedded system’s behavior
  Unified Modeling Language (UML) was developed as a computer science standard to develop object oriented system design (and is used in other areas)
  One tool, a state machine diagram (statechart), is used for modeling system behavior through finite state transitions.
  This will be a useful tool in developing your embedded system design

## Slide 24: System Architecture – UML Statechart Diagram
state nodes connected with transitions triggered by events
models dynamic aspects of a system
models how the system reacts to inputs
describes different states of the system
defines a state machine to model the system

## Slide 25: UML Behavioral State Machine
In extending the finite state machine structure
  A state models a situation during which some condition holds.
    a static situation such as an object waiting for some external event to occur.
      the event is said to “trigger” an action
    a dynamic conditions such as the process of performing some behavior.
    enters the state when the behavior commences and leaves it as soon as the behavior is completed
  The UML defines the following kinds of states:
    simple state,
    composite state.

## Slide 26: UML Behavioral State Machine
A simple state is a state that does not have sub states.
Drawn as a rectangle with rounded corners and the state name inside the rectangle.
  Simple state may have compartments:
    name compartment
    internal activities compartment
      holds a list of internal actions or state activities that are performed while in the state
      activity label identifies the circumstances under which the behavior will be invoked.

## Slide 27
A composite state is defined as state that has sub states
Composite state will have the following:
  name compartment
  internal activities compartment
  “decomposition compartment” (sub state sequence)
The first two compartments are the same as for simple state.
Decomposition refers to the nested structure of the state, diagrammed with internal states and transitions.
UML Behavioral State Machine

## Slide 28
If a large number of states are inside a composite state, they may not fit in the graphical space available for the diagram.
In that case, use a simple state graphic with a special "composite" icon.
This icon is a visual cue that the state has a decomposition that is not shown.
The contents of the composite state are shown in a separate diagram (could be on a different page)
UML Behavioral State Machine

## Slide 29
An initial pseudostate represents the symbol for a transition to the initial or default state.
An initial pseudostate is shown as a small solid filled circle.
Final state is a special kind of state signifying that the enclosing region (e.g., composite state) is completed.
E.g.,
UML Behavioral State Machine

## Slide 30
A transition is a directed relationship between a source state and a target state.
Transitions between states
  Reflect change in system from one state to another
  Expressed as an arrow directed from source to destination
Transition occurs when
  Event of interest to system occurs (triggered transition)
  System has completed some action and is ready to move to next state (triggerless transition)
An action may be associated with the the transition or it may be a transition to self
UML Behavioral State Machine

## Slide 31: UML Behavioral State Machine
from http://www.uml-diagrams.org
If the test fails, ATM goes into Out of Service state, otherwise there is triggerless transition to the Idle state.
In this state ATM waits for customer interaction.
The ATM state changes from Idle to Serving Customer when the customer inserts banking or credit card in the ATM's card reader.
On entering the Serving Customer state, the entry action readCard is performed.
The transition from Serving Customer state back to the Idle state could be triggered by cancel event or final state
Top level state machine Bank ATM is initially turned off. After the power is turned on, ATM performs startup action and enters Self Test state.

## Slide 32: UML Behavioral State Machine
from http://www.uml-diagrams.org
Customer Authentication and Transaction are composite states by themselves which is shown with hidden decomposition indicator icon.
Serving Customer state has triggerless transition back to the Idle state after transaction is finished.
The state also has exit action ejectCard which releases customer's card on leaving the state, no matter what caused the transition out of the state.
Serving Customer state is a composite state with sequential sub states Customer Authentication, Selecting Transaction and Transaction.

## Slide 33: Describing a system as a state machine
  List all possible states
  Declare all variables
  For each state, list possible transitions, with conditions, to other states
  For each state and/or transition, list associated actions
  For each state, ensure exclusive and complete exiting transition conditions
    No two exiting conditions can be true at same time
      Otherwise nondeterministic state machine
    One condition must be true at any given time
Here’s a couple of examples of a free drawing tools to support making UML behavioral state diagrams
https://wiki.gnome.org/action/show/Apps/Dia?action=show&redirect=Dia
http://argouml.tigris.org/

## Slide 34: Software Implementation of State Machine
#define S0 0
#define S1 1
...
#define SN N
void StateMachine() {
int state = S0; // or whatever is the initial state.
while (1) {
switch (state) {
case S0:
// Insert S0’s actions here & Insert transitions Ti leaving S0:
if( T0’s condition is true ) {state = T0’s next state; /*actions*/ }
if( T1’s condition is true ) {state = T1’s next state; /*actions*/ }
...
if( Tm’s condition is true ) {state = Tm’s next state; /*actions*/ }
break;
case S1:
// Insert S1’s actions here
// Insert transitions Ti leaving S1
break;
...
case SN:
// Insert SN’s actions here
// Insert transitions Ti leaving SN
break;
}
}
}